## Slide 1: VSS 2.0 proposal
Benjamin KLOTZ
 klotz@eurecom.fr
TPAC 2018, Lyon

## Slide 2: VSS in a nutshell
451 branches
1103 leaves:
  43 attributes
  1060 signals: (700 seat-related), 268 with unit,
Attribute/Signal
Body
Raindetection
Intensity
ADAS
Type: UInt8
Unit: percent
Description: “…”
Value: restriction or free
Cabin
Chassis
Drivetrain
OBD
Vehicle
Weight
Attribute
Signal
Signal entries
Examples:
Gearbox-sensed speed: .Drivetrain.Transmission.Speed
Engine speed: .Drivetrain.Engine.Speed
GPS-sensed speed: .Cabin.Infotainment.Speed
Left door lock: .Body.Row1.Door.Left.IsLocked
Right mirror tilt: .Cabin.Mirror.Right.Tilt

## Slide 3: VSS in 3 trees
Attribute
Branch
Vehicle
Branch
Body
Branch
Drivetrain
Branch
VehicleIdentification
Branch
VIN
Attribute
Signal
Branch
Body
Branch
Drivetrain
Branch
Vehicle
Branch
AverageSpeed
Signal
Private
Branch
BMW
Branch
HMI
Branch
PrivateSignal
??
- AverageSpeed:
type: Int32
min: -250
max: 250
unit: km/h
description: Average speed for the current trip
sensor: Odometer
- VehicleIdentification.VIN:
type: String
description: 17-character Vehicle Identification Number (VIN) as defined by ISO 3779

## Slide 4: Proposal
Branches are related by a “subbranch of” relationship
  The root (“Signal”, “Attribute”) is inappropriate
A URI construction scheme could use the VSS tree
Branch mismatch between branches from different trees
No way to define correctly the private tree
Merge trees to have only one VSS
Extend leaf metadata to differentiate signals and attributes
Use “/” instead of “.” in VSS names
In the end
VSS core
VSS private extention
VSS doc (JSON, VSI…)
Source mapping
(local data source)
VSS doc including:
URIs
Sources
All the metadata in a single tree

## Slide 5: (1) Merge trees to have only one vss
Proposal: future VSS structure
Current VSS structure
Attribute/Signal
Body
ADAS
Cabin
Chassis
Drivetrain
OBD
Vehicle
Vehicle
Body
ADAS
Cabin
Chassis
Drivetrain
OBD
Branches are related by a “subbranch of” relationship
The root (“Signal”, “Attribute”) is inappropriate

## Slide 6: (2) Extend the metadata on leaves
- AverageSpeed:
type: Int32
min: -250
max: 250
unit: km/h
description: Average speed for the current trip
sensor: Odometer
- VehicleIdentification.VIN:
type: String
description: 17-character Vehicle Identification Number (VIN) as defined by ISO 3779
VehicleIdentification.VIN:
function: Attribute
type: String
description: 17-character Vehicle Identification Number (VIN) as defined by ISO 3779
AverageSpeed:
function: Signal
type: Int32
min: -250
max: 250
unit: km/h
description: Average speed for the current trip
sensor: Odometer
Proposals:
A “function” entry that can be Signal/Attribute
A “function” entry that can be Attribute/Sensor/Actuator/Sensor-Actuator and the sensor/actuator entry removed
Another entry for optional practical information: diagnosis usage, stream usage

## Slide 7: (3) Include a URI construction scheme
VehicleIdentification.VIN:
function: Attribute
type: String
description: 17-character Vehicle Identification Number (VIN) as defined by ISO 3779
"Vehicle": {
"type": "branch",
"children": {
"VehicleIdentification": {
"type": "branch",
"children": {
"VIN": {
"description": "17-character Vehicle Identification Number (VIN) as defined by ISO 3779",
"type": "String",
"id": 40},
Generate JSON
VehicleIdentification.VIN:
function: Attribute
type: String
description: 17-character Vehicle Identification Number (VIN) as defined by ISO 3779
"Vehicle": {
"type": "branch",
"children": {
"VehicleIdentification": {
"type": "branch",
"children": {
"VIN": {
"description": "17-character Vehicle Identification Number (VIN) as defined by ISO 3779",
"type": "String",
"id": 40
“URI”: https://my.local.network/Vehicle/VehicleIdentification/VIN,
“source”: “my local source description”},
Generate JSON
Some source mapping
(Implementation-specific)

## Slide 8
Thank you for your attention
Do you have questions ?
Contact:
Benjamin Klotz
klotz@eurecom.fr